EMERGENCY ACTION PLAN (EAP)

OWNER OF DAM:

County of Louisa, Virginia

RECORD COPY	1	OF 	4

TABLE OF CONTENTS

Page No.

CERTIFICATIONS	3

NOTIFICATION FLOWCHART	4

STATEMENT OF PURPOSE	5

PROJECT DESCRIPTION	5

EMERGENCY DETECTION, EVALUATION, AND CLASSIFICATION	6-8

GENERAL RESPONSIBILITIES UNDER THE EAP	8-10

PREPAREDNESS	10-11

APPENDICES

A-1: DAM BREAK INUNDATION ZONE MAPS	12-20

A-2: RECORD OF HOLDERS OF CONTROL COPIES OF EAP	21

A-3: RECORD OF REVISIONS AND UPDATES MADE TO EAP	22

A-4: UNUSUAL OR EMERGENCY EVENT LOG	23

A-5: DAM EMERGENCY SITUATION REPORT	24

A-6: PROPERTIES WITHIN PMF DAM BREACH INUNDATION ZONE	25

A-7: PARCELS WITHIN PMF DAM BREACH INUNDATION ZONE	26-37

CERTIFICATIONS

By my signature, I acknowledge that I, or my representative, have reviewed this EAP and concur with the tasks and responsibilities assigned herein to me and my organization.

Dam Owner/Operator Designee’s Signature	Printed Name and Organization	Date

Emergency Services Coordinator’s Signature	Printed Name and Organization 	Date

Geoffrey L. Cowan / Dewberry Consultants LLC              06-04-13

Dam Owner’s Engineer’s Signature 	Printed Name and Organization	Date

STATEMENT OF PURPOSE

The purpose of this Emergency Action Plan (EAP) is to reduce the risk of personal injury and loss of human life as well as property damage during an unusual or emergency event at Gordonsville Dam.

PROJECT DESCRIPTION

Gordonsville Dam is a high hazard dam located on Dove Fork approximately 1 mile upstream of the confluence of Dove Fork and the South Anna River.  US Route 15 crosses the South Anna River just downstream of this confluence.  The DCR Dam Safety Inventory Number for Gordonsville Dam is 10923.  The dam creates an 80 acre impoundment used for flood control, water supply, and recreation.  The drainage area at the dam is approximately 15 square miles.  The normal pool volume is approximately 608 ac-ft at elevation 410.8 feet.  The flood storage capacity is approximately 1950 acre-feet at the emergency spillway crest elevation of 424.5 feet.  Downstream of the dam, the South Anna River flows for approximately 60 miles before joining the North Anna River to form the Pamunkey River.  All EAP elevations are referenced to NGVD 29 datum.

The main components of the dam are:

- Homogeneous earth embankment, approximately 500 feet long, with a crest elevation of approximately 429.9 feet and an approximate structural height of 42 feet.

- 2.5H:1V downstream embankment slope, 2.5H:1V upstream embankment slope above normal pool, 3H:1V upstream embankment slope below normal pool, with a 15 feet wide top width.  The dam embankment transitions to a guide dike along the emergency spillway at the north abutment contact.  A maintenance road crosses the auxiliary spillway inlet channel and terminates on top of the guide dike separating the dam embankment and emergency spillway.

- A 300 feet wide auxiliary spillway channel is cut into the left (looking downstream) dam abutment approximately 400 feet north of the principle spillway.  The auxiliary spillway crest elevation is 424.5 feet.

- A standard NRCS style two-way covered riser drop inlet spillway consisting a 5’ wide x 15’ long x 24’ high concrete riser with two 4’ wide x 1’-10” high orifices setting the normal pool at elevation 410.8 feet.  The riser weir crest elevation is set at elevation 419.3 feet

- Circular 60 inch diameter concrete outlet conduit, with an outlet invert elevation of 393 feet.

- 42 inch slide gate mounted to the principle spillway riser is used for draining the impoundment.  Three 10” gate valves exist at various levels for water supply withdrawal.

Gordonsville Dam was designed by the USDA Soil Conservation Service in 1966 and was constructed in 1969.

EMERGENCY DETECTION, EVALUATION, AND CLASSIFICATION

This section provides a discussion of the procedures for timely and reliable Detection, Evaluation and Classification of emergency situations for Gordonsville Dam.

Detection

Detection of an unusual or emergency event provides information to assist the Dam Owner/Operator in determining the appropriate emergency level for the event.

Unusual or emergency events may be detected by:

- Observations at or near the dam by government personnel, landowners, visitors to the Dam, or the public.

- Forewarning of conditions, which may cause an unusual event or emergency event at the dam (for example, a severe weather or flash flood forecast issues by the National Weather Service).

Evaluation and Classification

After an unusual or emergency event is detected or reported, the Dam Owner/Operator is responsible for classifying the event into one of the following three (3) Emergency Stage Conditions:

Stage I Condition; Non-emergency, unusual event, slowly developing:

This situation is not normal. However, it has yet to threaten the operation or structural integrity of the dam but could if it continues to develop.  An example is a flood watch or heavy continuous rain or excessive flow of water from ice or snow melts.

For flood events, a Stage I Condition is initiated when the National Weather Service has issued a flood watch, heavy continuous rainfall is predicted, or the reservoir pool is at the weir crest of the principal spillway riser (i.e. water-surface elevation = 419.3 ft or 8.5 foot above normal).

During a Stage I Condition the Dam Owner/Operator shall monitor conditions at the dam at least once every 6 hours at a minimum. In addition, the following shall occur:

- The Dam Owner/Operator shall contact his engineer to investigate the situation and to provide feedback.

- The Dam Owner/Operator shall contact the VA DCR Dam Safety Official to make him aware that the EAP has been enacted at a Stage I Condition and will keep him informed of conditions as they develop.

Stage II Condition; Potential Dam failure situation, rapidly developing:

This situation may eventually lead to dam failure and flash flooding downstream, but there is not an immediate threat of dam failure.  An example is an activation of the emergency spillway or potential for a dam overtopping/breach.

For flood events, a Stage II Condition is initiated when the reservoir pool reaches the auxiliary spillway crest (i.e. water-surface elevation = 424.5 ft).

During a Stage II Condition the Dam Owner/Operator shall monitor conditions at the Dam at least once every hour. In addition the following shall occur:

- The Dam Owner/Operator shall contact his engineer to investigate the situation, provide feedback, and recommend preventative actions that can be taken if needed.

- The Dam Owner/Operator shall contact and put the Emergency Services Coordinator on alert.

- The Emergency Services Coordinator shall contact and put Emergency Services on alert (i.e. police and fire) to notify potential evacuees and to close roads as needed if flooding increases downstream of the Dam. Contact information of individuals in the dam inundation zone to be evacuated are listed on Appendix A-6.

- The Dam Owner/Operator shall contact and put VDOT’s Resident Engineer on alert as flooding may impact Route 15 (James Madison Highway), Route 22 (Louisa Road), Route 695 (Hamilton Road), and Route 613 (Poindexter Road), Route 649 (Byrd Mill Road), Route 208 (Courthouse Road), Route 604 (Roundabout Road) and Route 646 (Yanceyville Road).

- The Dam Owner/Operator shall contact the VA DCR Dam Safety Official to make him aware that the EAP has been enacted at a Stage II Condition and will keep him informed of conditions as they develop.

Stage III Condition; Urgent - Dam failure appears to be imminent or is in progress:

This is an extremely urgent situation when a dam failure is occurring or obviously is just about to occur and cannot be prevented. This situation is also applicable when flow through the spillways is causing or about to cause high danger flooding to people and roads, or if flow through the emergency spillway is resulting in severe erosion with an advancing headcut that is threatening the emergency spillway crest.

For flood events, a Stage III Condition is initiated when the reservoir pool reaches one (1) foot below the top of dam (i.e. water-surface elevation = 428.9 ft) or when severe erosion is occurring in the emergency spillway resulting in an advancing headcut that is threatening to erode through the emergency spillway crest.

During a Stage III Condition the Dam Owner/Operator shall continuously monitor conditions at the Dam. In addition the following shall occur:

- The Dam Owner/Operator shall contact and put the Emergency Services Coordinator on alert.

- The Emergency Services Coordinator shall contact and put Emergency Services on alert (i.e. police and fire) to notify potential evacuees and to close roads as needed if flooding increases downstream of the Dam. Contact information of individuals in the dam inundation zone to be evacuated are listed on Appendix A-6.

- The Dam Owner/Operator shall contact and put VDOT’s Resident Engineer on alert as flooding will impact Route 15 (James Madison Highway), Route 22 (Louisa Road), Route 695 (Hamilton Road), and Route 613 (Poindexter Road), Route 649 (Byrd Mill Road), Route 208 (Courthouse Road), Route 604 (Roundabout Road) and Route 646 (Yanceyville Road).

- The Dam Owner/Operator shall contact his engineer to investigate the situation and to provide feedback.

- The Dam Owner/Operator shall contact the VA DCR Dam Safety Official to make him aware that the EAP has been enacted at a Stage III Condition and will keep him informed of conditions as they develop.

GENERAL RESPONSIBILITIES UNDER THE EAP

Dam Owner/Operator

- Responsible for developing, maintaining, exercising and implementing this EAP – serves as the EAP’s coordinator. Ensures that a copy of the EAP has been filed with Louisa County Emergency Services Coordinator.

- Responsible for updating and resubmitting the EAP immediately upon becoming aware of necessary changes to keep the EAP workable.

- Responsible for inspecting and maintaining Gordonsville Dam in accordance with its Operation and Maintenance Plan and Schedules as approved by VA DCR Division of Dam Safety and Floodplain Management.

- Responsible as the observer at Gordonsville Dam during weather events that are anticipated to produce high water conditions at the dam or during observed “sunny day” events that may pose a risk to the structural integrity of the dam (e.g. seepage with cloudy discharge and increasing flow rate).

- Responsible for assigning alternate observer(s) at Gordonsville Dam during Emergency Stage Conditions, if needed.

- Responsible for classifying all Emergency Stage Conditions into the appropriate category (i.e. Stage I Condition, Stage II Condition or Stage III Condition) as described in this EAP.

- Responsible for executing the EAP Notification Flowchart.

- Responsible for providing updates to the Emergency Services Coordinator during Emergency Stage Conditions.

- Responsible for implementing preventative actions to take during an emergency Stage II Condition, if needed.

- Responsible for providing leadership to assure the EAP is reviewed and updated annually and copies of the revised EAP are distributed to all record holders of the EAP.

- Responsible for arranging and coordinating a Drill at least once every six (6) years as described in this EAP under the section entitled, Preparedness.

Emergency Services Coordinator

- Responsible for serving as the primary contact person for coordination of all emergency actions.

- Responsible for assigning a qualified alternate Emergency Services Coordinator that is equally familiar with this EAP in the event that the Emergency Services Coordinator of record for this EAP is absent during an emergency situation.

- Responsible for contacting Emergency Services (i.e. police and fire) as necessary based on the Emergency Stage Condition provided by the Dam Owner/Operator.

- Responsible for maintaining communications with the media and public as appropriate.

- Responsible for deciding when to terminate the Emergency Stage Conditions based on feedback from Emergency Services (i.e. police and fire) and the Dam Owner/Operator.

- Responsible for participating in an annual review and update of the EAP.

- Responsible for participating in a Drill as arranged by the Dam Owner/Operator.

- Responsible for coordinating a representative(s) from Emergency Services (i.e. Police and Fire) to participate in the Drill as arranged by the Dam Owner/Operator.

Emergency Services (i.e. Police and Fire)

- Responsible for maintaining communication with the Emergency Services Coordinator throughout the emergency.

- Responsible for notifying potential evacuees in the dam inundation zone during an Emergency Stage II Condition as directed by the Emergency Services Coordinator or as deemed necessary based on conditions in the field at and downstream of the Dam.  Contact information of individuals in the dam inundation zone to be evacuated are listed on Appendix A-6.

- Responsible for carrying out evacuations in the dam inundation zone during an Emergency Stage III Condition as directed by the Emergency Services Coordinator or as deemed necessary based on conditions in the field at and downstream of the Dam. Contact information of individuals in the dam inundation zone to be evacuated are listed on Appendix A-6.

- Responsible for road closures in the dam inundation zone during an Emergency Stage II or Stage III Condition as directed by the Emergency Services Coordinator or as deemed necessary based on conditions in the field at and downstream of the Dam.

- Responsible for re-opening roads after the emergency has been terminated by the Emergency Services Coordinator.

Dam Owner’s Engineer

- Responsible for advising the Dam Owner/Operator on the appropriate Emergency Stage Condition (i.e. Stage I, Stage II or Stage III), if requested and if time permits.

- Responsible for advising the Dam Owner/Operator on possible preventative actions to take if an Emergency Stage II Condition occurs, if time permits.

- Responsible for participating in a Drill as arranged by the Dam Owner/Operator.

PREPAREDNESS

EAP Annual Review

The Dam Owner/Operator will review and, if needed, update the EAP by September 1 of each year.  At a minimum the Dam Owner/Operator will perform the following tasks:

- Contact all participants of the EAP and let them know that the EAP is undergoing an annual review.

- Confirm all names and phone numbers of participants referenced in the EAP.

- Ask all participants who received a copy of the EAP if they know where the EAP is kept and if he/she understands his/her responsibilities as described in the EAP.

- Request all participants who received a copy of the EAP to review it; mark it up; and resubmit it back to the Dam Owner/Operator as appropriate.

- Incorporate all changes as appropriate and send a revised copy of the EAP to all record holders of the EAP.

Revisions

The Dam Owner/Operator is responsible for updating the EAP documents.  The EAP document held by the Dam Owner/Operator is the master document. When revisions occur, the Dam Owner/Operator will incorporate all changes made to the EAP and issue a revised copy to each of the record document holders. The record document holders are responsible for keeping their copy of the revised EAP on file.  Outdated versions of the EAP shall be immediately discarded to avoid any confusion with past revisions.

EAP Drill

The Dam Owner/Operator will host and facilitate a Drill of the EAP at least once every six years.  The Drill will consist of a meeting, including a table-top exercise. Attendance should include the Dam Owner/Operator, Emergency Services Coordinator, Dam Owner’s Engineer, VA DCR Dam Safety Official and at least one representative of the local law enforcement agency. Other organizations that may be involved with an unusual or emergency event at the dam are encouraged to participate at the discretion of the Dam Owner/Operator.  Meeting participants will visit the dam during the Drill to familiarize themselves with the dam site before the table-top exercise begins.

The table-top exercise will begin with the facilitator presenting a scenario of an unusual or emergency event at the Dam.  The scenario will be developed prior to the exercise.  Once the scenario has been presented, the participants will discuss the responses and actions that they would take to address and resolve the scenario. The facilitator will control the discussion, ensuring realistic responses and developing the scenario throughout the exercise. After the table-top exercise, the Drill will be reviewed and discussed. The Dam Owner/Operator will prepare a written summary of the Drill and revise the EAP as necessary.

Termination

Based on feedback from the Dam Owner/Operator and Emergency Services (i.e. Police and Fire), the Emergency Services Coordinator is responsible for formally terminating EAP operations.

Prior to termination of an Emergency Stage III Condition that has not caused actual dam failure, the Dam Owner/Operator and his engineer will inspect the dam to determine whether any damage has occurred that could potentially result in loss of life, injury, or property damage.  The results of this inspection will be passed along to the Emergency Services Coordinator.

The Dam Owner/Operator shall assure that the Dam Emergency Situation Report (Appendix A-5) is completed to document the emergency event and all the actions taken. The Dam Owner/Operator shall distribute copies of the completed report to VA DCR Division of Dam Safety and Floodplain Management and his engineer.

APPENDIX A-2

##### RECORD OF HOLDERS OF CONTROL COPIES OF THIS EAP

| Copy Number | Organization | Person Receiving Copy |
| --- | --- | --- |
| 1 | LOUISA COUNTY WATER AUTHORITY 23 LOUDIN LANE, P.O. BOX 9 LOUISA, VIRGINIA 23093 | DEAN RODGERS |
| 2 | DEWBERRY CONSULTANTS LLC 13575 HEATHCOTE BLVD., SUITE 130 GAINESVILLE, VA 20155 | GEOFFREY COWAN |
| 3 | LOUISA COUNTY 1 WOOLFOLK AVE., P.O. BOX 160 LOUISA, VA 23093 | SCOTT KEIM |
| 4 | DCR (REGION 5) DAM SAFETY 900 NATURAL RESOURCES DR., ROOM 2028 CHARLOTTESVILLE, VA 22903 | ROBERT VANLIER |

##### APPENDIX A-3

##### RECORD OF REVISIONS AND UPDATES MADE TO EAP

| Revision Number | Date | Revisions Made | Who |
| --- | --- | --- | --- |
| 00 | 06/04/13 | Create original EAP for Gordonsville Dam | Dewberry Consultants LLC |

APPENDIX A-4

UNUSUAL OR EMERGENCY EVENT LOG

(To be completed during the emergency)

Dam Name:   GORDONSVILLE DAM	County:   LOUISA COUNTY

When and how was the event detected?

Weather conditions:

General description of the emergency situation: ____________________________________________

Emergency level determination: ______________  Made by: _________________________________

ACTIONS AND EVENT PROGRESSION

| Date | Time | Action/Event Progression | Taken By |
| --- | --- | --- | --- |

Report Prepared by: _______________________________________  Date: _______________

APPENDIX A-5

## DAM EMERGENCY SITUATION REPORT

(To be completed following the termination of the emergency)

Dam Name:  GORDONSVILLE DAM 		County:   LOUISA COUNTY

Date: 	Time:

Weather Conditions:

General Description of Emergency Situation:

Area(s) of Dam Affected:

Extent of Dam Damage:

Possible Cause(s):

Effect on Dam’s Operation:

Initial Reservoir Elevation:	 Time:

Maximum Reservoir Elevation:	 Time:

Final Reservoir Elevation:	 Time:

Description of area flooded downstream/Damages/injuries/loss of life:

Other Data and Comments:

Observer’s name and telephone number:

Report Prepared by: ________________________________________       Date: ______________

APPENDIX A-6

HABITABLE STRUCTURES WITHIN PMF DAM BREACH INUNDATION ZONE *

| Inundation Map ID # | Building # | Parcel # | Building Address | Parcel Owner | Owner Address (if different than building address) | Telephone # | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 |  | 21 1 4 | 3479 JAMES MADISON HIGHWAY | MORRISON, BRIAN R |  | 540-832-2129 |  |
| 2 | 11808 | 37 28B | 1490 HAMILTON ROAD | LAMB, TROY ALLYN |  | 540-967-9284 |  |
| 3 | 11556 | 37 25A | 1611 HAMILTON ROAD | WILLIS, PATRICIA D & K ANDREW |  | 540-967-1776 |  |
| 4 | 14890 | 37 18 | 5446 EAST JACK JOUETT ROAD | MCINTIRE, MARTHA A |  | 540-967-0522 |  |
| 5 | 15353 | 37 32 | 5061 POINDEXTER ROAD | ATKINS, DONALD & FRANCES | P O BOX 98 TREVILIANS VA 23170 | 540-967-1561 | No Occupant |
| 6 | 15302 | 37 32 | 5071 POINDEXTER ROAD | ATKINS, DONALD & FRANCES | P O BOX 98 TREVILIANS VA 23170 |  | Out buildings on same farm (No Occupant) |
| 7 | 17350 | 53 12 4 | 4116 EAST JACK JOUETT ROAD | PATTON, DAN M & ROBIN W | P O BOX 977 LOUISA VA 23093 | 540-967-2619 |  |
| 8 | 17623 | 53 12 3 | 4108 EAST JACK JOUETT ROAD | HARTLEY, DAVID W & HOLLY C | 11432 LONG MEADOW DR GLEN ALLEN VA 23059 | 540-967-2594 |  |
| 9 | 17996 | 53 4 | 4028 EAST JACK JOUETT ROAD | FOSTER CREEK BAPTIST CHURCH |  | 540-967-2940 |  |
| 10 | 18455 | 53 95 | 3890 EAST JACK JOUETT ROAD | PASS, CLAY Q |  | 540-697-0312 |  |
| 11 | 18233 | 53 96A | 3688 EAST JACK JOUETT ROAD | BRICKEY, CAROL ANN & SCHATZKI, ALFRED EDWARD |  | 540-967-2212 |  |
| 12 |  | 54 50A | 985 SUGARPLUM ROAD | HICKS, CARRIE & DERRICK | 915 SUGARPLUM RD LOUISA VA 23093 | 540-967-2971 |  |
| 13 | 18662 | 55 5 B3 | 1936 BYRD MILL ROAD | GILLESPIE, JAY B & TRACEY C | 2004 BYRD MILL RD LOUISA VA 23093 | 540-967-5261 |  |
| 14 | 19193 | 55 81 | 883 BICKLEY ROAD | HAWK, RICHARD C & SHIRLEY K | 267 BLUEBERRY LN LOUISA VA 23093 | 540-967-2675 |  |
| 15 | 19687 | 55 74 | 4239 COURTHOUSE ROAD | TASHJIAN, JOHN R | 243 DANIELS RD RICHMOND VA 23238 |  | Recreational Cabin (No Occupant) |
| 16 | 20023 | 56 92 | 343 HORSESHOE FARM ROAD | SYDNOR, WALTER NEAL |  | 540-967-0160 |  |
| 17 | 22355 | 69 5 29 | 776 BEND OF RIVER LANE | EL, CRAIG EUGENE & NICKEL, JENNIFER SUZANNE |  |  | Under construction (No Occupant) |
| 18 | 22411 | 56 6 24 | 761 BEND OF RIVER LANE | LAPEL, LARRY & LINDA J |  |  | Uninhabited (empty) |
| 19 | 22410 | 70 8 12 | 111 BEND OF RIVER LANE | MCNUTT, CHARLES D & DONNA F |  | 540-967-2079 |  |
| 20 |  | 70 51 | 723 MT. AIRY ROAD | ARMSTRONG, KAREN CHAPMAN | P O BOX 236 MINERAL VA 23117 | 540-894-4903 |  |
| 21 | 23728 | 71 41 | 334 MT. AIRY ROAD | MICKENS, JOHNETTA I | C/O JOHNETTA BELL 334 MT AIRY RD LOUISA VA 23093 | 540-894-0535 |  |
| 23 | 24648 | 70 13 1D | 10653 SHANNON HILL ROAD | WIESE, LEROY W & JOAN M |  | 540-894-9428 |  |

*  All building, parcel, and owner information taken from Louisa County GIS records

APPENDIX A-7

PARCELS WITHIN PMF DAM BREACH INUNDATION ZONE *

| Item # | PIN | Owner | Owner2 | Owner Address | Owner City, State | Owner Zip |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | 21 2 | COLUMBIA GAS TRANSMISSION |  |  | CHARLESTON, WV | 25317 |
| 2 | 70 45 | BAKER, DONALD F & CAROL A |  | 1493 MT AIRY RD | LOUISA VA | 23093 |
| 3 | 55 9 B | JOHNSON, BRIAN ANTHONY & |  | JOHNSON, DORIS NAOMIA | LOUISA, VA | 23093 |
| 4 | 21 90 | CRAWFORD, LINWOOD K JR & BETTY F |  |  | GORDONSVILLE, VA | 22942 |
| 5 | 21 1 4 | MORRISON, BRIAN R |  |  | GORDONSVILLE, VA | 22942 |
| 6 | 9 39C | COOKE, WILLIAM A INC |  |  | LOUISA, VA | 23093 |
| 7 | 9 39C | COOKE, WILLIAM A INC |  |  | LOUISA, VA | 23093 |
| 8 | 22 36 | COOKE, WILLIAM A |  |  | LOUISA, VA | 23093 |
| 9 | 9 120 | WALTON LUMBER COMPANY |  |  | MINERAL, VA | 23117 |
| 10 | 21 95 | ALBERTS, WILLIAM C K & HOWARD K |  | 11807 LOUISA RD | GORDONSVILLE, VA | 22942 |
| 11 | 55 102 | DOVE, JEREMIAH C & JENNIFER L |  |  | LOUISA, VA | 23093 |
| 12 | 22 4 1 | GREEN SPRINGS ESTATES LLC | C/O BONDSTONE VENTURES INC | P O BOX 6100 | CHARLOTTESVILLE, VA | 22906 |
| 13 | 21 1 3B | CABLE HOLDCO EXCHANGE III LLC | C/O COMCAST CORPORATION | P O BOX 173838 | DENVER, CO | 80217 |
| 14 | 21 11 C | SHAW, BARBARA S |  | 428 WALDROP RD | GORDONSVILLE VA | 22942 |
| 15 | 10 17V | LEISURE CAPITAL CORPORATION |  |  | BOCA RATON, FL | 33431 |
| 16 | 21 97 | ADAMS, JAMES E & COLLEEN E |  | 9810 VARUS PL | UPPER MARLBORO, MD | 20772 |
| 17 | 9 39 | SHAW, GRETCHEN J TRUSTEE FOR | RAYMOND B SHAW FAMILY TRUST | 3028 JAMES MADISON HWY | GORDONSVILLE VA | 22942 |
| 18 | 9 39B | ANDERSON, CHARLES A & LINDA M |  |  | GORDONSVILLE, VA | 22942 |
| 19 | 21 91 | CRAWFORD, LINWOOD K JR & BETTY F |  |  | GORDONSVILLE, VA | 22942 |
| 20 | 21 89 | CRAWFORD, LINWOOD K JR & BETTY F |  |  | GORDONSVILLE, VA | 22942 |
| 21 | 22 23 | SILBERMAN, MICHAEL J & CAROLYN W |  | 14708 LOUISA RD | LOUISA VA | 23093 |
| 22 | 21 11 D | FREDERICK, WANDA SHAW |  |  | BEALETON, VA | 22712 |
| 23 | 21 91 | CRAWFORD, LINWOOD K JR & BETTY F |  |  | GORDONSVILLE, VA | 22942 |
| 24 | 9 39 | SHAW, GRETCHEN J TRUSTEE FOR | RAYMOND B SHAW FAMILY TRUST | 3028 JAMES MADISON HWY | GORDONSVILLE VA | 22942 |
| 25 | 9 39A | COOKE, WILLIAM A INC |  |  | LOUISA, VA | 23093 |
| 26 | 21 92 | MOSES, CHARLES A & EDITH M |  | 4503 W GRACE ST | RICHMOND VA | 23230 |
| 27 | 21 11 B | SHAW, DAVID WILLIAM |  | 3018 JAMES MADISON HWY | GORDONSVILLE VA | 22942 |
| Item # | PIN | Owner | Owner2 | Owner Address | Owner City, State | Owner Zip |
| 28 | 22 4 2 | GREEN SPRINGS ESTATES LLC | C/O BONDSTONE VENTURES INC | P O BOX 6100 | CHARLOTTESVILLE, VA | 22906 |
| 29 | 21 94 | MOSES, CHARLES A & EDITH M |  | 4503 W GRACE ST | RICHMOND VA | 23230 |
| 30 | 69 48 | DOWDY, MATTHEW E & JESSICA S |  |  | LOUISA, VA | 23093 |
| 31 | 69 50 | TALLEY GOODWIN LLC | C/O MR TASOS GALIOTOS | WILLCOX & SAVAGE ATTS | VIRGINIA BEACH, VA | 23462 |
| 32 | 21 93 | MOSES, CHARLES A & EDITH M |  | 4503 W GRACE ST | RICHMOND VA | 23230 |
| 33 | 22 4 3 | GREEN SPRINGS ESTATES LLC | C/O BONDSTONE VENTURES INC | P O BOX 6100 | CHARLOTTESVILLE, VA | 22906 |
| 34 | 69 49 | ANDERSON, TOMMY L |  |  | LOUISA, VA | 23093 |
| 35 | 22 37 | SIMS, JACK | C/O JEAN P SMITH | 813 SPRING VALLEY DR | FALMOUTH, VA | 22405 |
| 36 | 21 96 | ALBERTS, ROBERT F D & ELIZ M FRAZER |  | 12145 LOUISA RD | GORDONSVILLE, VA | 22942 |
| 37 | 22 35 | HISTORIC GREEN SPRINGS INC | C/O ANGELO LOMASCOLO TREAS | PO BOX 1685 | LOUISA, VA | 23093 |
| 38 | 22 26 | HOWLAND, ELIZABETH DONIPHAN PURCELL |  | 14103 LOUISA RD | LOUISA VA | 23093 |
| 39 | 22 3 A | VIRGINIA VERMICULITE LLC |  | P O BOX 70 | LOUISA, VA | 23093 |
| 40 | 22 13 | BRANDY LTD | C/O MRS HILL | 302 HARRISON AVE | WILLIAMSBURG VA | 23185 |
| 41 | 22 1 1 | WHITE, ZIEGLER O & YVONNE W |  |  | LOUISA, VA | 23093 |
| 42 | 22 4 5 | HISTORIC GREEN SPRINGS INC | C/O ANGELO LOMASCOLO TREAS | P O BOX 1685 | LOUISA, VA | 23093 |
| 43 | 37 29 | ROSSON, CHARLES S & ELIZABETH |  | 5728 POINDEXTER RD | LOUISA, VA | 23093 |
| 44 | 55 74 | TASHJIAN, JOHN R |  | 243 DANIELS RD | RICHMOND VA | 23238 |
| 45 | 22 14 | NININGER, ELGIN H JR & | NININGER, SCOTT QUINCY |  | COLONIAL BEACH, VA | 22443 |
| 46 | 22 25 | PIERCE, ERIN J |  |  | ALEXANDRIA, VA | 22314 |
| 47 | 22 4 4 | GRACELAND LLC | C/O BONDSTONE VENTURES INC | P O BOX 6100 | CHARLOTTESVILLE, VA | 22906 |
| 48 | 37 2 | HEIMER, HANNE-BJORG TRUSTEE OF THE |  | HEIMER FAMILY & HEIMER SURVIVOR'S TRUST | LOUISA, VA | 23093 |
| 49 | 55 107 | HARLOW, AUBREY JAMES & THELMA L |  |  | LOUISA, VA | 23093 |
| 50 | 38 27 | ROSSON, CHARLES S |  | 5728 POINDEXTER RD | LOUISA, VA | 23093 |
| 51 | 22 19 | SILBERMAN, MICHAEL J & CAROLYN W |  | 14708 LOUISA RD | LOUISA VA | 23093 |
| 52 | 22 15 | DOWELL, W E & LEWIS A & BENNIE | C/O MICHAEL DOWELL | P O BOX 487 | KESWICK, VA | 22947 |
| 53 | 37 25C | WINDSOR, JAY W & LYNN F |  | 1663 HAMILTON RD | LOUISA VA | 23093 |
| 54 | 37 25A | WILLIS, PATRICIA D & K ANDREW |  |  | LOUISA, VA | 23093 |
| 55 | 22 16 | GARDNER, JUDSON MORGAN & | ELAINE BRAY |  | ORANGE, VA | 22960 |
| 56 | 22 17 | DAVIS, MARGIE D & MICHAEL C |  |  | MIDLOTHIAN, VA | 23113 |
| 57 | 37 21 | DAVIS, MARGIE D & MICHAEL C |  |  | MIDLOTHIAN, VA | 23113 |
| Item # | PIN | Owner | Owner2 | Owner Address | Owner City, State | Owner Zip |
| 58 | 37 1 | MANNING, PAUL B & DIANE L |  |  | TROY, VA | 22974 |
| 59 | 37 27B | BALOGH, BRIAN H & KATHLEEN CRAIG |  | 6319 POINDEXTER RD | LOUISA VA | 23093 |
| 60 | 37 22 | DAVIS, MARGIE D & MICHAEL C |  |  | MIDLOTHIAN, VA | 23113 |
| 61 | 37 36 | CHAPMAN, KATHARINE M | C/O STEPHEN C HARRIS, ATTORNEY | P O BOX 486 | LOUISA, VA | 23093 |
| 62 | 37 20 | SMITH, LEONARD I & FRANCES M |  | 1414 HARVEY RD | FARRAGUT TN | 37922 |
| 63 | 37 23 | DAVIS, MARGIE D & MICHAEL C |  |  | MIDLOTHIAN, VA | 23113 |
| 64 | 37 25 | MITCHELL, JOHN W & DOROTHY |  | 2121 HAMILTON RD | LOUISA VA | 23093 |
| 65 | 37 27 | HANEY, MARY E & | HANEY, EVERETT ROY JR TRUSTEES |  | LOUISA, VA | 23093 |
| 66 | 37 26 | SCHARF, JAMES D & JULIA S |  | 2106 HAMILTON RD | LOUISA VA | 23093 |
| 67 | 37 25B | KELIH, RICHARD E JR |  |  | LOUISA, VA | 23093 |
| 68 | 37 19 | WOOD, LANCE D |  |  | ALEXANDRIA, VA | 22303 |
| 69 | 37 19B | REYNOLDS, RONALD F |  |  | LOUISA, VA | 23093 |
| 70 | 70 52A | WEBER, KYRA L |  |  | LOUISA, VA | 23093 |
| 71 | 70 40 | PAYNE, GEORGE L |  |  | LOUISA, VA | 23093 |
| 72 | 55 7 B | NEWMAN, JOHN W JR |  |  |  | 0 |
| 73 | 37 32 | ATKINS, DONALD & FRANCES |  |  | TREVILIANS, VA | 23170 |
| 74 | 70 39A | SHORT, RAYMOND DON JR & | JUANITA JOAN MATKINS | 624 YANCEYVILLE RD | LOUISA VA | 23093 |
| 75 | 54 49 | PERKINS, JOHN C & HAZEL P |  | 1414 MYRADARE DR | RICHMOND VA | 23229 |
| 76 | 54 47 | HARLOW, MICHAEL JUAN & | CHAPMAN, LINDA GAIL |  | LOUISA, VA | 23093 |
| 77 | 38 29A | WILLIAMS, ALAN |  |  | CONYERS, GA | 30012 |
| 78 | 38 92 | MACCAULEY, EVA VIRGINIA TRUSTEE |  |  | LOUISA, VA | 23093 |
| 79 | 54 3 | PERKINS, DELMAR D JR |  | 1167 DELL PERKINS RD | LOUISA VA | 23093 |
| 80 | 55 77 | DANIEL, LAWRENCE R |  |  | FREDERICKSBURG, VA | 22407 |
| 81 | 55 81 | HAWK, RICHARD C & SHIRLEY K |  |  | LOUISA, VA | 23093 |
| 82 | 69 15 7 | BAKER, CLACY E |  | 14016 CAMPAIGN CT | FREDERICKSBURG VA | 22407 |
| 83 | 70 8 12 | MCNUTT, CHARLES D & DONNA F |  | 111 BEND OF RIVER LN | LOUISA VA | 23093 |
| 84 | 69 5 30 | HALL, WILLIAM V |  |  | LOUISA, VA | 23093 |
| 85 | 69 5 29 | NICKEL, CRAIG EUGENE & | NICKEL, JENNIFER SUZANNE | 776 BEND OF RIVER LN | LOUISA, VA | 23093 |
| 86 | 56 6 24 | LAPEL, LARRY & LINDA J |  | 761 BEND OF RIVER LANE | LOUISA, VA | 23093 |
| 87 | 70 15 | HARRIS, DANNY R & PATTI P |  |  | LOUISA, VA | 23093 |
| Item # | PIN | Owner | Owner2 | Owner Address | Owner City, State | Owner Zip |
| 88 | 70 17 | PAYNE, GEORGE LEE SR |  |  | LOUISA, VA | 23093 |
| 89 | 70 13 | TWIN OAKS COMMUNITY | C/O TAXES | 138 TWIN OAKS RD | LOUISA, VA | 23093 |
| 90 | 37 15A | SOMOZA, NANCY DANIEL TRUSTEE |  | 846 CENTRAL BRANCH RD | LOUISA VA | 23093 |
| 91 | 56 28 | DANIEL, EVELYN PATTON |  |  | LOUISA, VA | 23093 |
| 92 | 55 121 | WINSTON HALL LC | WILLIAM I SANDERSON, REG AGENT C/O PURCELL & PURCELL ATTORNEYS | P O BOX 126 | LOUISA, VA | 23093 |
| 93 | 55A 1 3 | DICK PURCELL LAND CATTLE & | TIMBER CORPORATION |  | LOUISA, VA | 23093 |
| 94 | 56 45 | PERKINS, E N | C/O LLOYD JUNIOR PERKINS | 7941 ASHFORD BLVD | LAUREL, MD | 20707 |
| 95 | 55 11 | PAYNE, DOUGLAS W |  | 1231 BICKLEY RD | LOUISA VA | 23093 |
| 96 | 37 29B | ENGLEMAN, NANCY A |  |  | LOUISA, VA | 23093 |
| 97 | 37 29A | MCCAFFREY, MICHAEL |  | PO BOX 1005 | MADISON VA | 22727 |
| 98 | 37 19A | REYNOLDS, RONALD F |  |  | LOUISA, VA | 23093 |
| 99 | 37 6 | REYNOLDS, RONALD F |  |  | LOUISA, VA | 23093 |
| 100 | 37 30 | ROSSON, CHARLES S & ELIZABETH |  | 5728 POINDEXTER RD | LOUISA, VA | 23093 |
| 101 | 37 31 | WCF ANNEX LLC |  |  | LOUISA, VA | 23093 |
| 102 | 37 7 | SOMOZA, NANCY DANIEL TRUSTEE |  | 846 CENTRAL BRANCH RD | LOUISA VA | 23093 |
| 103 | 37 18 | MCINTIRE, MARTHA A |  | 5446 E JACK JOUETT RD | LOUISA VA | 23093 |
| 104 | 37 34 | ROSSON, CHARLES S & ELIZABETH |  | 5728 POINDEXTER RD | LOUISA, VA | 23093 |
| 105 | 55 9 A | GEWIRTZ, ANISCETA DEJESUS ET ALS | C/O FELIPE DEJESUS | 4 JOLIE CT | RANDALLSTOWN, MD | 21133 |
| 106 | 37 10A | JOHNSON, AUDREY ANN |  | 807 CENTRAL BRANCH RD | LOUISA VA | 23093 |
| 107 | 37 7 | SOMOZA, NANCY DANIEL TRUSTEE |  | 846 CENTRAL BRANCH RD | LOUISA VA | 23093 |
| 108 | 37 41 | COMMONWEALTH GAS PIPELINE CORP |  |  | RICHMOND, VA | 23235 |
| 109 | 37 35 | ATKINS, M MAURY & TERESA N |  |  | LOUISA, VA | 23093 |
| 110 | 54 59 | PERKINS, RONALD ANDERSON ET ALS |  | 2441 BYRD MILL RD | LOUISA VA | 23093 |
| 111 | 53 3 | WEBB, LESLIE S JR & | WEBB, CAROLYN W |  | RICHMOND, VA | 23238 |
| 112 | 55 94 | HARDIN, ELDA MAE |  |  | LOUISA, VA | 23093 |
| 113 | 56 6 31 | SHAO, TIFFANY C |  |  | CHESTERFIELD, VA | 23832 |
| 114 | 57 11 14 | CHERRY, NATASHA D |  |  | LOUISA, VA | 23093 |
| 115 | 54 2 | PERKINS, BERNARD EARL & CLARICE G |  | 738 DELL PERKINS RD | LOUISA VA | 23093 |
| 116 | 53 5 | WEBB, LESLIE S JR & | WEBB, CAROLYN W |  | RICHMOND, VA | 23238 |
| 117 | 54 43 | O'CONNOR, JAMES A & NINA J |  |  | LOUISA, VA | 23093 |
| Item # | PIN | Owner | Owner2 | Owner Address | Owner City, State | Owner Zip |
| 118 | 55 11 4 | PERKINS, CLAUDIA B |  | 403 BICKLEY RD | LOUISA VA | 23093 |
| 119 | 56 94 | HOPKINS, STEVEN B & CRYSTI |  |  | LOUISA, VA | 23093 |
| 120 | 37 47 | ROSSON, CHARLES S |  | 5728 POINDEXTER RD | LOUISA, VA | 23093 |
| 121 | 70 8C | HARRIS, DANNY R & PATTI P |  |  | LOUISA, VA | 23093 |
| 122 | 53 12 4 | PATTON, DAN M & ROBIN W |  | P O BOX 977 | LOUISA VA | 23093 |
| 123 | 37 34A | ATKINS, DONALD L |  | TRUSTEES OF BEREA BAPTIST CHURCH | LOUISA, VA | 23093 |
| 124 | 37 10 | JOHNSON, AUDREY ANN & | ROSE MARIE HAWLEY | 807 CENTRAL BRANCH RD | LOUISA VA | 23093 |
| 125 | 37 45 | COMMONWEALTH GAS PIPELINE CORP |  |  | RICHMOND, VA | 23235 |
| 126 | 37 17 | MCINTIRE, MARTHA A |  | 5446 E JACK JOUETT RD | LOUISA VA | 23093 |
| 127 | 37 39 | CHAPMAN, KATHARINE M | C/O STEPHEN C HARRIS, ATTORNEY | P O BOX 486 | LOUISA, VA | 23093 |
| 128 | 56 35 | HOPKINS, ROY E & MARY JO |  |  | LOUISA, VA | 23093 |
| 129 | 37 33 | BEREA BAPTIST CHURCH |  |  |  | 0 |
| 130 | 37 16 | CHAPMAN, KATHARINE M | C/O STEPHEN C HARRIS, ATTORNEY | P O BOX 486 | LOUISA, VA | 23093 |
| 131 | 38 29 | WILLIAMS, ALAN |  |  | CONYERS, GA | 30012 |
| 132 | 37 40 | EARLEY, LAVERNE M TRUSTEE | THE LAVERNE M EARLEY REVOC TRUST |  | SILVER SPRING, MD | 20906 |
| 133 | 37 9 | JOHNSON, AUDREY ANN |  | 807 CENTRAL BRANCH RD | LOUISA VA | 23093 |
| 134 | 37 37 | CHAPMAN, KATHARINE M | C/O STEPHEN C HARRIS, ATTORNEY | P O BOX 486 | LOUISA, VA | 23093 |
| 135 | 55 16 | KENNY, ANDREW R & JEANNIE TRUSTEES |  |  | LOUISA, VA | 23093 |
| 136 | 37 11 | SOMOZA, NANCY DANIEL TRUSTEE |  | 846 CENTRAL BRANCH RD | LOUISA VA | 23093 |
| 137 | 55 17 | MCGEHEE, JOHN C & MARK A TRUSTEES | C/O CHARLES F MCGEHEE | 25 BUCKINGHAM COMMON | WAYNESBORO, VA | 22980 |
| 138 | 55 119 | O'BRIEN, JOSEPH F III & DANA E | C/O DANA O'BRIEN | 11010 MARCLIFF RD | ROCKVILLE, MD | 20852 |
| 139 | 70 54A | MORGAN, JOSEPH H & MARY ANGELA | TRS OF THE MORGAN LIVING TRUST | 8207 WESTMEATH LN | RICHMOND VA | 23227 |
| 140 | 70 13 1A | BRITTON, VIRGINIA F |  | 9314 GREENFORD DR | RICHMOND VA | 23294 |
| 141 | 37 38 | CHAPMAN, KATHARINE M | C/O STEPHEN C HARRIS, ATTORNEY | P O BOX 486 | LOUISA, VA | 23093 |
| 142 | 55 11 3 | BICKLEY, CECIL WAYNE |  | 614 BICKLEY RD | LOUISA VA | 23093 |
| 143 | 56 6 35 | SPENCER, JOSEPH A & JOYCE S ET AL | C/O MARVIS A HAZEL | 828 CHATSWORTH DR | NEWPORT NEWS, VA | 23601 |
| 144 | 71 30 | MUDZO, MICHAEL A & DIANE S |  |  | BURKE, VA | 22015 |
| 145 | 37 36A | CHAPMAN, KATHARINE M | C/O STEPHEN C HARRIS, ATTORNEY | P O BOX 486 | LOUISA, VA | 23093 |
| 146 | 38 29B | CAMPBELL, KATHLYN J & LEONARD L |  |  | NEW MARKET, VA | 22844 |
| 147 | 37 15 | SOMOZA, NANCY DANIEL TRUSTEE |  | 846 CENTRAL BRANCH RD | LOUISA VA | 23093 |
| Item # | PIN | Owner | Owner2 | Owner Address | Owner City, State | Owner Zip |
| 148 | 37 12 | SOMOZA, NANCY DANIEL TRUSTEE |  | 846 CENTRAL BRANCH RD | LOUISA VA | 23093 |
| 149 | 69 15 8 | RANKIN, OWEN K & MICHELLE J |  |  | BOONTON, NJ | 7005 |
| 150 | 69 1 | WINSTON HALL LC | WILLIAM I SANDERSON, REG AGENT C/O PURCELL & PURCELL ATTORNEYS | P O BOX 126 | LOUISA, VA | 23093 |
| 151 | 70 16 | PAYNE, GEORGE L |  |  | LOUISA, VA | 23093 |
| 152 | 38 30 | PERKINS, D D JR |  |  | LOUISA, VA | 23093 |
| 153 | 71 13 2 | HENLEY, WARREN S & ANNA R |  |  | LOUISA, VA | 23093 |
| 154 | 54 6 | PERKINS, DELMAR D JR |  | 1167 DELL PERKINS RD | LOUISA VA | 23093 |
| 155 | 55 103 | ADMIRAL'S POINT LLC |  | 20 COURTHOUSE SQ STE 106 | ROCKVILLE, MD | 20850 |
| 156 | 55 23 | TALLEY, JOYCE G & ET ALS |  | 5707 ELLISVILLE DR | LOUISA VA | 23093 |
| 157 | 56 92 | SYDNOR, WALTER NEAL |  | 343 HORSESHOE FARM RD | LOUISA VA | 23093 |
| 158 | 55 111 | MOUBRAY, BONNIE H |  | 4858 COURTHOUSE RD | LOUISA VA | 23093 |
| 159 | 53 93 | SIMMONS, MICHAEL SEAN & OKSANA A |  | 3535 EAST JACK JOUETT RD | LOUISA VA | 23093 |
| 160 | 56 6 34 | ANDERSON, TRUDY A |  |  | VIENNA, VA | 22180 |
| 161 | 54 9A | ROBINS, EVELYN |  | 165 ADVANCE MILLS RD | RUCKERSVILLE VA | 22968 |
| 162 | 56 6 33 | PRATT, LARRY D |  | 7747 WAGON RUN RD | GLOUCESTER VA | 23061 |
| 163 | 56 6 20 | GAUSE, KENNETH R & SHANNON C |  |  | POWHATAN, VA | 23139 |
| 164 | 56 6 19A | BOAT DOCK AREA |  |  |  | 0 |
| 165 | 56 6 19 | DOOLEY PLUMBING & HEATING SOUTH INC |  |  | PALMYRA, VA | 22963 |
| 166 | 70 49 | BROYLES, DORIS C & WILLIAM C |  | 8605 WASHINGTON AVE | ALEXANDRIA VA | 22309 |
| 167 | 70 11 C | BOOKER, GRANVILLE B & LAURIE V |  | 2400 RIVANCRUST DR | CHARLOTTESVILLE VA | 22901 |
| 168 | 53 6 | WEBB, LESLIE S JR & | WEBB, CAROLYN W |  | RICHMOND, VA | 23238 |
| 169 | 69 15 4 | RANKIN, OWEN K & MICHELLE J |  |  | BOONTON, NJ | 7005 |
| 170 | 54 58 | PERKINS, RONALD ANDERSON ET ALS |  | 2441 BYRD MILL RD | LOUISA VA | 23093 |
| 171 | 55 112 | ADMIRAL'S POINT LLC |  | 20 COURTHOUSE SQ STE 106 | ROCKVILLE, MD | 20850 |
| 172 | 71 13 1 | WEEDON, JAMES R & TINA C |  |  | LOUISA, VA | 23093 |
| 173 | 70 52 | BREZNICK, WILLIAM & LOLA |  | 10891 SHANNON HILL RD | LOUISA VA | 23093 |
| 174 | 53 12 2 | MOORE, MICHAEL D & ADELIA REBECCA |  | 4132 E JACK JOUETT RD | LOUISA VA | 23093 |
| 175 | 70 54B | MORGAN, JOSEPH H TRUSTEE |  | 2301 HILLIARD RD | RICHMOND VA | 23228 |
| 176 | 54 67 | HARLOW, LYNDA F |  |  | LOUISA, VA | 23093 |
| 177 | 53 7 | WEBB, GEORGE W & LOIS W |  |  | LOUISA, VA | 23093 |
| Item # | PIN | Owner | Owner2 | Owner Address | Owner City, State | Owner Zip |
| 178 | 54 7 | CHODOSH, MARGARET P & LANCE |  |  | GAINESVILLE, FL | 32605 |
| 179 | 54 55 | ROSSON, MELVIN H |  | 811 SUGARPLUM RD | LOUISA VA | 23093 |
| 180 | 54 1 | PERKINS, BERNARD EARL & CLARICE G |  | 738 DELL PERKINS RD | LOUISA VA | 23093 |
| 181 | 54 50 | ROSSON, ERNEST G ET ALS |  | 981 SUGARPLUM RD | LOUISA VA | 23093 |
| 182 | 55 10 | PERKINS, CLAUDIA B |  | 403 BICKLEY RD | LOUISA VA | 23093 |
| 183 | 55 15 | MARKS, RUSSELL E & ROBERT S |  | 1617 BICKLEY RD | LOUISA VA | 23093 |
| 184 | 55 76 | CARTER, RICHARD | C/O EXEC TRAVIS E DANIEL JR | 1914 VANDOVER RD | RICHMOND, VA | 23229 |
| 185 | 54 68 | BROADWATER, CHARLES E & BETTY M |  | 565 SUGARPLUM RD | LOUISA VA | 23093 |
| 186 | 54 9 | PERKINS, ROY DENNIS SR |  | 3128 E JACK JOUETT RD | LOUISA VA | 23093 |
| 187 | 54 9B | ROBINS, EVELYN |  | 165 ADVANCE MILLS RD | RUCKERSVILLE VA | 22968 |
| 188 | 54 71A | PERKINS, DOUGLAS C |  | 291 SUGARPLUM RD | LOUISA VA | 23093 |
| 189 | 54 73 | PERKINS, HARVEY D & SHARON |  | 409 SUGARPLUM RD | LOUISA VA | 23093 |
| 190 | 54 71C | PERKINS, ROBERT W |  |  | LOUISA, VA | 23093 |
| 191 | 55 5 B3 | GILLESPIE, JAY B & TRACEY C |  |  | LOUISA, VA | 23093 |
| 192 | 54 71B | PERKINS, HAZEL P & JOHN C |  | 1414 MYRADARE DR | RICHMOND VA | 23229 |
| 193 | 56 40 | CARON, THOMAS L III & JEANNE E |  |  | LOUISA, VA | 23093 |
| 194 | 55 19 | PERKINS, LEWIS & MARY E |  | 3909 SHUTTERLEE MILL RD | STAUNTON VA | 24401 |
| 195 | 54 8 | O'CONNOR, JAMES A & NINA J |  |  | LOUISA, VA | 23093 |
| 196 | 56 44 | TRICE, NORRIS & MARY TRICE ET ALS | C/O CALVIN TRICE | P O BOX 148 | LOUISA, VA | 23093 |
| 197 | 55 18 | KENNY, ANDREW R & JEANNIE TRUSTEES |  |  | LOUISA, VA | 23093 |
| 198 | 54 74 | HARLOW, BESSIE E, JEAN G HARLOW & | EVA MAE WILLIAMS |  | LOUISA, VA | 23093 |
| 199 | 56 26 | NUCKOLS REALTY LLC | C/O ELIZABETH N NUCKOLS | 2140 MANAKIN RD | MANAKIN SABOT, VA | 23103 |
| 200 | 55 11 1 | BICKLEY, CECIL WAYNE |  | 614 BICKLEY RD | LOUISA VA | 23093 |
| 201 | 55 105 | AUSTIN PROFIT SHARING PLAN | FOR JESSE R & J ANNE AUSTIN |  | LANHAM, MD | 20706 |
| 202 | 56 27 | O'BRIEN, ELIZABETH B | O'BRIEN, ELIZABETH B TRUSTEE | P O BOX 1637 | LOUISA, VA | 23093 |
| 203 | 55 106 | BICKLEY, LLOYD D ET ALS |  |  | LOUISA, VA | 23093 |
| 204 | 54 32 | HARLOW, MELVIN M |  |  | LOUISA, VA | 23093 |
| 205 | 56 43 | ROBERTS, WILLIAM WALE |  | 10 GRANITE AVE | RICHMOND VA | 23226 |
| 206 | 54 101 | HARLOW, BESSIE E, JEAN G HARLOW & | EVA MAE WILLIAMS |  | LOUISA, VA | 23093 |
| 207 | 54 44 | HARLOW, J R JR, E F & W W ESTATE | C/O BESSIE E HARLOW | 1237 BYRD MILL RD | LOUISA, VA | 23093 |
| Item # | PIN | Owner | Owner2 | Owner Address | Owner City, State | Owner Zip |
| 208 | 56 39 | KNIFIC, DENIS & SUZANNE S TRS |  |  | SOUTH LEBANON, OH | 45065 |
| 209 | 54 100 | HARLOW, BESSIE E, JEAN G HARLOW & | EVA MAE WILLIAMS |  | LOUISA, VA | 23093 |
| 210 | 54 33 | HARLOW, MELVIN M |  |  | LOUISA, VA | 23093 |
| 211 | 56 38 | DEIKE, SELENE K |  |  | LOUISA, VA | 23093 |
| 212 | 55 118 | SNIDER, JOHN N ET ALS | C/O BRENDA S KANARY | 3566 WILLOWBROOK RD | BUMPASS VA | 23024 |
| 213 | 53 12 3 | HARTLEY, DAVID W & HOLLY C |  |  | GLEN ALLEN, VA | 23059 |
| 214 | 56 93 | HOPKINS, STEVEN B & CRYSTI B |  |  | LOUISA, VA | 23093 |
| 215 | 56 102 | DANIELS, GRAHAM R & NANCY F |  |  | LOUISA, VA | 23093 |
| 216 | 56 29 | HAMILTON, NINA A & | HAMILTON, MELVINIA P |  | KING WILLIAM, VA | 23086 |
| 217 | 55 75 | CARTER, RICHARD | C/O EXEC TRAVIS E DANIEL JR | 1914 VANDOVER RD | RICHMOND, VA | 23229 |
| 218 | 56 95 | HOPKINS, ROY E & MARY JO |  |  | LOUISA, VA | 23093 |
| 219 | 56 93A | HOPKINS, STEVEN B & CRYSTI B |  |  | LOUISA, VA | 23093 |
| 220 | 56 37 | HOPKINS, ROY E & MARY JO |  |  | LOUISA, VA | 23093 |
| 221 | 53 96 | BRICKEY, RALPH A & VIVIAN C & | BRICKEY, JAMES A | 3130 E JACK JOUETT RD | LOUISA, VA | 23093 |
| 222 | 54 56 | ROSSON, ERNEST G ET ALS |  | 981 SUGARPLUM RD | LOUISA VA | 23093 |
| 223 | 71 32 | CLARK, KELLY J JR & CASSIE D |  | P O BOX 1174 | LOUISA VA | 23093 |
| 224 | 56 144 | BATEMAN, DAVID M |  | 1805 BLACKHAWK PL | CHESAPEAKE VA | 23321 |
| 225 | 69 2 | ROSSON, WAYNE E |  | 511 HAROLDS DR | MANAKIN SABOT VA | 23103 |
| 226 | 56 96 | HOPKINS, ROY E & MARY JO |  |  | LOUISA, VA | 23093 |
| 227 | 55 125 | WINSTON HALL LC | WILLIAM I SANDERSON, REG AGENT C/O PURCELL & PURCELL ATTORNEYS | P O BOX 126 | LOUISA, VA | 23093 |
| 228 | 53 4 | FOSTER CREEK BAPTIST CHURCH |  |  | LOUISA, VA | 23093 |
| 229 | 70 3 B | SMALL, VIRGIE |  |  |  | 0 |
| 230 | 70 8 | TAYLOR, THOMAS J & LESLIE S |  |  | OILVILLE, VA | 23129 |
| 231 | 69 84 | SISK, L JANE |  | 4301 HENDRICKS DR | WOODBRIDGE, VA | 22193 |
| 232 | 56 30 | HOPKINS, ROY E & MARY JO |  |  | LOUISA, VA | 23093 |
| 233 | 70 41B | PAYNE, GEORGE L |  |  | LOUISA, VA | 23093 |
| 234 | 56 34 | PRYOR, BRENDA H |  | 3376 PRYOR RD | GOOCHLAND VA | 23063 |
| 235 | 56 98 | HOPKINS, STEVEN B & CRYSTI B |  |  | LOUISA, VA | 23093 |
| 236 | 56 33 | HOPKINS, OVERTON W TRUSTEE | HOPKINS FAMILY TRUST U/T/D |  | LOUISA, VA | 23093 |
| 237 | 56 101 | HOPKINS, GRACE G | C/O BRENDA H PRYOR | 3376 PRYOR RD | GOOCHLAND, VA | 23063 |
| Item # | PIN | Owner | Owner2 | Owner Address | Owner City, State | Owner Zip |
| 238 | 57 30 | HARRISON, WILLIAM |  |  | LOUISA, VA | 23093 |
| 239 | 56 143 | BATEMAN, DAVID M |  | 1805 BLACKHAWK PL | CHESAPEAKE VA | 23321 |
| 240 | 70 8 8 | GRIFFITH, MAVERICK B | C/O CHARLES D MCNUTT | 111 BEND OF THE RIVER LN | LOUISA, VA | 23093 |
| 241 | 69 9 4 | NEWSOME, J WARREN & DEBORAH M |  |  | WAYNESBORO, VA | 22980 |
| 242 | 70 8 9 | BWI CONSTRUCTION LLC |  | 10417 FLAT BRANCH DR | RICHMOND VA | 23233 |
| 243 | 70 8 11 | THOMAS, ROBBIE M |  |  | LOUISA, VA | 23093 |
| 244 | 56 6 18 | PRATT, PAUL E & ELIZABETH W |  | 300 COOK RD | YORKTOWN VA | 23690 |
| 245 | 56 6 17 | WHEELER, CHARLES W |  |  | LOUISA, VA | 23093 |
| 246 | 56 6 36 | MURPHY, PATRICK G & | DELONTI, ROBERT J & DONNA | 550 DEVON PL | LONG BEACH CA | 90807 |
| 247 | 57 11 16 | WHEELER, CHARLES W |  |  | LOUISA, VA | 23093 |
| 248 | 56 6 21 | DOOLEY PLUMBING & HEATING SOUTH INC |  |  | PALMYRA, VA | 22963 |
| 249 | 56 6 32 | HAYNES ANDERSON ASSOCIATES | C/O JOSEPH DOODY | P O BOX 889 | ORANGE, VA | 22960 |
| 250 | 69 9 3 | RODGERS, DEAN C & | KIRK-RODGERS, SANDRA D |  | LOUISA, VA | 23093 |
| 251 | 56 6 22 | MITCHELL, SANDY WILLIAM JR & | MITCHELL, SUSAN DIANE & | MITHCELL, TERRY WILMER | FREDERICKSBURG, VA | 22405 |
| 252 | 57 11 15 | EARLEY, MAYLON JAMES JR |  |  | LOUISA, VA | 23093 |
| 253 | 70 6 | SOPHIA HOUSE |  | P O BOX 710 | LOUISA VA | 23093 |
| 254 | 69 1 A | PLEASANTS, BRADLEY T SR & NANCY M & |  | BRADLEY T JR & MICHAEL G PLEASANTS | LOUISA, VA | 23093 |
| 255 | 57 11 13 | JORDAN, EDWIN D & NICOLE M |  | 15500 HARROWGATE RD | CHESTER VA | 23831 |
| 256 | 56 6 23 | RUEHL, WILLIAM ET ALS | C/O JOHN LYNN FOSTER | 6 PAULA DR | NEWPORT NEWS, VA | 23608 |
| 257 | 69 9 2 | CLUNE, THOMAS E JR & SANDRA A |  |  | LOUISA, VA | 23093 |
| 258 | 69 5 26 | EDWARDS, STEVEN R & ALICE F |  |  | LANEXA, VA | 23089 |
| 259 | 69 5 27 | EDWARDS, STEVEN R & ALICE F LAWS |  |  | LANEXA, VA | 23089 |
| 260 | 70 8 6 | SNEAD, LARRY |  |  | CHARLOTTESVILLE, VA | 22911 |
| 261 | 70 8 10 | DAVIS, PEGGY J |  |  | FREDERICKSBURG, VA | 22408 |
| 262 | 69 5 25 | WALSH, DAVID K |  |  | RICHMOND, VA | 23233 |
| 263 | 69 5 28 | WEATHERHOLTZ, LUKE AARON & | HARRIS, SARA MACEL |  | LOUISA, VA | 23093 |
| 264 | 70 1 | ATKINS, MINNIE B ET ALS | C/O LAWRENCE A BADGETT | 1773 YANCEYVILLE RD | LOUISA, VA | 23093 |
| 265 | 69 15 6 | CARDINAL, SHARON M |  |  | LOUISA, VA | 23093 |
| 266 | 69 9 1 | PAINTER, MICHAEL E & ALVIN A |  | 4905 DAFFODIL CR | GLEN ALLEN VA | 23060 |
| 267 | 69 15 5 | JOHNSON, CURTIS A SR |  | PO BOX 731 | CHARLOTTESVILLE VA | 22901 |
| Item # | PIN | Owner | Owner2 | Owner Address | Owner City, State | Owner Zip |
| 268 | 69 9 5 | WYATT, JAMES F |  | 6200 CLUB RD | RICHMOND VA | 23228 |
| 269 | 69 15 3 | BEASLEY, LISA C & CURTIS A CARTER |  | 4320 ROUNDABOUT RD | LOUISA VA | 23093 |
| 270 | 69 15 2 | SEWELL, DENNIS I & KARIN M |  | 4248 ROUNDABOUT RD | LOUISA VA | 23093 |
| 271 | 69 15 1 | MHS ENTERPRISES, INC |  | PO BOX 948 | VIRGINIA BEACH VA | 23451 |
| 272 | 69 77 | JONES, DANIEL A |  | 8355 LIMEKILN PIKE | WYNCOTE PA | 19095 |
| 273 | 70 9 | ATKINS, MINNIE B ET ALS | C/O LAWRENCE A BADGETT | 1773 YANCEYVILLE RD | LOUISA, VA | 23093 |
| 274 | 70 10 | HARRIS, DANNY R & PATTI P |  |  | LOUISA, VA | 23093 |
| 275 | 70 42 | HENSHAW, DENYSE HAINES & KENNETH | SAMUEL |  | LOUISA, VA | 23093 |
| 276 | 71 39A | RICHARDSON, BOBBY GENE |  | 304 MT AIRY RD | LOUISA VA | 23093 |
| 277 | 71 42 | SUDDUTH, TIMOTHY & MARJORIE |  | 272 MT AIRY RD | LOUISA VA | 23093 |
| 278 | 71 41 | MICKENS, JOHNETTA I | C/O JOHNETTA BELL | 334 MT AIRY RD | LOUISA, VA | 23093 |
| 279 | 70 41 | PAYNE, GEORGE L |  |  | LOUISA, VA | 23093 |
| 280 | 71 13 9 | JACOBS, CAROL M |  | 181 MT AIRY RD | LOUISA VA | 23093 |
| 281 | 70 50 | DISOSWAY, JOHN JUSTICE & REBECCA M |  |  | LOUISA, VA | 23093 |
| 282 | 69 85 | TALLEY GOODWIN LLC | C/O MR TASOS GALIOTOS | WILLCOX & SAVAGE ATTS | VIRGINIA BEACH, VA | 23462 |
| 283 | 71 39 | LANUZO, ANTHONY |  | 8636 WOODVIEW DR | SPRINGFIELD VA | 22153 |
| 284 | 70 8B | COLLIER, PAUL JR |  |  | MANAKIN SABOT, VA | 23103 |
| 285 | 70 51 | ARMSTRONG, KAREN CHAPMAN |  |  | MINERAL, VA | 23117 |
| 286 | 70 3 A | SMALL, VIRGIE M |  |  | MINERAL, VA | 23117 |
| 287 | 70 5 A | SADLER, H PHILIP JR & | MARGARET MURPHY | 1241 VIGOR RD | LOUISA VA | 23093 |
| 288 | 70 51A | RENALDS, SCOTT SANDY |  | P O BOX 740 | LOUISA VA | 23093 |
| 289 | 71 13 5 | FIELDS, BRANDON L & ALISHA G |  |  | LOUISA, VA | 23093 |
| 290 | 70 14 | HARRIS, DANNY R & PATTI P |  |  | LOUISA, VA | 23093 |
| 291 | 70 11 | BATCHELOR, DEBORAH A & | JONES, LINDA G | 5405 CHARLES CITY RD | RICHMOND VA | 23231 |
| 292 | 70 52B | WIESE, LEROY W & JOAN M |  |  | LOUISA, VA | 23093 |
| 293 | 70 13 1D | ROBERTSON, H CARTER & DENISE M |  | 10637 SHANNON HILL RD | LOUISA VA | 23093 |
| 294 | 54 17 23 | CG HOMES LLC |  |  | MIDDLEBURG, VA | 20118 |
| 295 | 70 39 | GOSSETT, GARY W & RUTH C |  |  | LOUISA, VA | 23093 |
| 296 | 70 41A | PAYNE, GEORGE L |  |  | LOUISA, VA | 23093 |
| 297 | 70 12 | ANDERSON, TOMMY L |  |  | LOUISA, VA | 23093 |
| Item # | PIN | Owner | Owner2 | Owner Address | Owner City, State | Owner Zip |
| 298 | 70 13 1C | WU & ZHU LLC |  | 203 GUNBY DR | RICHMOND VA | 23229 |
| 299 | 70 13 1B | MCCLUNG, CRAIG LEE & | TOURANGEAU, ELIZABETH | PO BOX 497 | MINERAL VA | 23117 |
| 300 | 70 55 | THOMPSON, DONALD M & SUZANNE M |  | P O BOX 1759 | LOUISA VA | 23093 |
| 301 | 37 28 | RIGBY, MATTHEW GARDNER & | RIGBY, MARSHALL B |  | RICHMOND, VA | 23226 |
| 302 | 37 28B | LAMB, TROY ALLYN |  | 1490 HAMILTON RD | LOUISA, VA | 23093 |
| 303 | 70 20 | BADGETT LLC | C/O MR TASOS GALIOTOS | WILLCOX & SAVAGE ATTS | VIRGINIA BEACH, VA | 23462 |
| 304 | 56 138 | PRATT, PAUL E & ELIZABETH W |  | 300 COOK RD | YORKTOWN VA | 23690 |
| 305 | 56 103 | HENDERSON, THOMAS J JR & MARY H | HODGES & LINDA FOX CRAM |  | HUNTINGTON, WV | 25701 |
| 306 | 56 104 | HENDERSON, THOMAS J JR & MARY H | HODGES & LINDA FOX CRAM |  | HUNTINGTON, WV | 25701 |
| 307 | 56 141 | PRATT, PAUL E & ELIZABETH W & |  | PRATT, LARRY DEAN | YORKTOWN, VA | 23690 |
| 308 | 55 17 5 | LLOYD, DWAYNE A & CONNIE H |  |  | GORDONSVILLE, VA | 22942 |
| 309 | 55 17 6 | BYRD POINT LLC |  | 355 SPRING LN | CHARLOTTESVILLE VA | 22903 |
| 310 | 55 17 7 | MENJE, JARAMIE A & CHARLENE M |  | 97 BYRD POINT LN | LOUISA VA | 23093 |
| 311 | 55 17 2 | MOLLENHAUER, DAVID & PHYLLIS W |  | 126 BYRD POINT LN | LOUISA, VA | 23093 |
| 312 | 55 17 3 | BYRD POINT LLC |  | 355 SPRING LN | CHARLOTTESVILLE VA | 22903 |
| 313 | 55 17 4 | MEEDS, HEATHER K |  | 188 BYRD POINT LN | LOUISA, VA | 23093 |
| 314 | 53 94 | PASS, CLAY Q |  |  | LOUISA, VA | 23093 |
| 315 | 53 95 | PASS, CLAY Q |  |  | LOUISA, VA | 23093 |
| 316 | 55 114 | BICKLEY, LLOYD D ET ALS |  |  | LOUISA, VA | 23093 |
| 317 | 69 12 A | PURCELL, CHARLES F & PURCELL, R G & | DAUGHTERS LAND & DEVELOPMENT INC |  | LOUISA, VA | 23093 |
| 318 | 54 17 24 | CG HOMES LLC |  |  | MIDDLEBURG, VA | 20118 |
| 319 | 21 1 4 | MORRISON, BRIAN R |  |  | GORDONSVILLE, VA | 22942 |
| 320 | 70 7 | QUARLES, N J | C/O ALBERT A QUARLES | 5460 W OLD MOUNTAIN RD | LOUISA, VA | 23093 |
| 321 | 37 28A | LAMB, TROY ALLYN |  | 1490 HAMILTON RD | LOUISA, VA | 23093 |
| 322 | 54 17 12 | CG HOMES LLC |  |  | MIDDLEBURG, VA | 20118 |
| 323 | 54 17 13 | CG HOMES LLC |  |  | MIDDLEBURG, VA | 20118 |
| 324 | 54 50A | HICKS, CARRIE & DERRICK |  |  | LOUISA, VA | 23093 |
| 325 | 54 50B | ROSSON, MARK ALLEN & | ROSSON, JANAL ASHLEY JONES |  | LOUISA, VA | 23093 |
| 326 | 53 96A | BRICKEY, CAROL ANN & | SCHATZKI, ALFRED EDWARD |  | LOUISA, VA | 23093 |
| 327 | 22 3 R | LEISURE CAPITAL CORPORATION |  |  | BOCA RATON, FL | 33431 |
| Item # | PIN | Owner | Owner2 | Owner Address | Owner City, State | Owner Zip |
| 328 | 10 17T | LEISURE CAPITAL CORPORATION |  |  | BOCA RATON, FL | 33431 |

*  All parcel and owner information taken from Louisa County GIS records

# Text boxes

Gordonsville Dam

Virginia DCR Dam Safety Inventory No. 10923

Hazard Potential Classification:  High

Louisa County, Virginia

APPENDIX A-1

ATTACHMENT 2